## Slide 1
Carbon-Aware SRAM Optimization via Simulation-Based Design-Space Exploration Subtitle
Minimizing CO2 Emissions Per Bit Access through Design-Space Mapping

## Slide 2
Proposed Idea Flow Chart
SRAM Simulation
Carbon Modelling
Power, delay, SNM Data
CO2 emission calculation
Pareto-Based Mode Classification
Turbo
Normal
Eco
Retention
Machine Learning Model
Train predictive model
Estimate power, delay, CO2
Digital Twin Simulation
Dynamic power mode control
Workload change
Performance needs
Carbon constraints

## Slide 3
Detailed Description
SRAM Simulation
Purpose: perform SPICE-based cct simulations on a std 6T SRAM cell
Inputs:
Transistor sizing variations
VDD
Outputs:
Dynamic power (switching energy)
Leakage power (standby energy)
Access delay
Static noise margin (SNM)
Goal: collect accurate electrical behavior under diverse operating cond.
2. Carbon Modeling
Purpose: Translate energy consumption into carbon emission
Inputs:
Energy data from simulations
Real-world carbon intensity
Outputs:
CO2/access
CO2/s

## Slide 4
Detailed Description
Pareto-based Mode Classification
Purpose: use pareto analysis to assign each design point into 1 of 4 SRAM power modes
Inputs:
3 performance metrics: power, delay, CO2/access
Classification Targets:
Turbo (high speed, high power, high CO2)
Normal (balanced)
Eco (low power, moderate delay)
Retention (min leakage, high delay)
Output: design map showing which sizing/ VDD combos fall into which mode
Machine Learning Model
Purpose: train a model to predict power, delay, and CO2 for new SRAM settings
Inputs:
Dataset from simulation stage (features = VDD, sizing; targets = power, delay, CO2)
Models:
- Choose most suitable one (polynomial, random forest, etc)
Outputs:
Trained predictive model
Used for fast estimation in system simulations

## Slide 5
Detailed Description
Digital Twin Simulation
Purpose: use ML model to simulate syst.-level SRAM behavior in real time under dynamic cond.
Functionality:
Predict SRAM behavior under new workloads
Choose best power mode based on:
Performance demand
Current grid carbon intensity
Use Case:
Enables real-time mode switching in SRAM systems
Emulates hardware behavior without full SPICE re-simulation